## Slide 1: Design Methodology for Silicon-Accurate Jitter Analysis for 28nm Interface IP for 100GBASE-LR4 Applications
Alan Rogers - Analog Bits
Nandu Bhagwan – GHz Circuits, Inc
Ravi Subramanian - Berkeley Design Automation
October 16, 2012
Space for affiliation logo

## Slide 2: Introduction
2
Presenting verification results of Integer-N PLL IP
Three way collaboration between:
  Analog Bits: 28nm IP macro for 100 Gigabit Ethernet
  TSMC: Reference flow development and 28nm process
  BDA: Device Noise Analysis in the AFS Platform

## Slide 3: SerDes IP Targets SoC Applications
Multi-Rate, multi-Protocol, programmable SERDES IP
Minimize power, latency and area
Stringent verification challenges (phase noise & jitter)
PLL determines the
phase noise & jitter
specs
PLL

## Slide 4: PLL IP Verification Challenges
Need to precisely analyze and predict PLL Phase noise & jitter
PLL Simulations are very expensive (time & compute resources)
Traditional SPICE simulators do not have performance and capacity
Need full-spectrum device noise to accurately verify phase noise
Need nanometer SPICE accuracy to predict silicon performance
PLL noise sources

## Slide 5: PLL Analysis Methods: Pros and Cons
Simulation Method
Architectural
Block-level
Transient Noise
Closed-Loop
Effective Analysis Range
Full Band
Full band
(Low freq limited by runtime)
Spur Evaluation
Freq Domain: No
Time Domain: Yes
Yes
Noise Modeling of RefClk, Supply, etc.
Yes
Needs to be added to netlist
Simulation Setup/Complexity
Simple
Simple
Convergence Issues
Minimal
None
Accuracy
Implementation Dependent
Nanometer SPICE
Simulation Time
Fast
Intensive for low
offset frequencies

## Slide 6: The Verification Platform
Analog Bits Selects Analog FastSPICE™ (AFS) Platform

## Slide 7: AFS in TSMC AMS Reference Flow

## Slide 8: SERDES under a Bump Pitch
Analog Bits SERDES

## Slide 9: Block Level AFS + TF Aggregation Example of Block Level Extraction for VCO
Circuit Inventory
Analysis Conditions
Simulation Runtime
  23 mins on 4 Xeon X5460 @3.16GHz CPUs
Good OSCNOISE and AFS TN correlation
 | VCO 1 | VCO 2
VDD | 1.8V | 1.2V
FOUT | 13.7 – 13.8 GHz | 
Conditions | SS, Lo T (0º) | 
Types of Analysis | Transient Noise, OSCNOISE | 
Carrier = 14GHz
Phase Noise dBc/Hz
Relative Frequency – Hz (log10)
bsim4v5_0 280
bsource_c 257
bsource_i 187
capacitor 203
diode 2
inductor 180
mutual inductor 6
resistor 6
vsource 50

## Slide 10: Silicon Measurements
SS | Low Amp | Med Amp | Hi Amp
Low BW | 384 |  | 373
Med BW |  | 366 | 
Hi BW | 333 |  | 307
FF | Low Amp | Med Amp | Hi Amp
Low BW | 378 |  | 337
Med BW |  | 360 | 
Hi BW | 303 |  | 285

## Slide 11: Silicon Correlation (Best Case) FF Wafers, High BW, High VCO Amp
VCO Dominated
Noise floor of Meas. Eqpt.
Refclk Dominated
FF Wafers
V: 1.2V, 1V
Room Temp
BW ~ 4.2MHz
Amp ~ 0.55V
Fout = 7GHz
Jitter = 285 fs
LEGEND:
LMEAS
LSIM - Total
LSIM – REF
LSIM – VCO
LSIM - OPSTG
Phase Noise dBc/Hz

## Slide 12: Silicon Correlation (Worst Case) SS Wafers, Low BW, Low VCO Amp
VCO Dominated
Output Stages Dominated
Remember this hump ?
Amplitude Modulation
SS Wafers
V: 1.2 V, 1 V
Room Temp
BW ~ 450 KHz
Amp ~ 0.35 V
Fout = 7 GHz
Jitter = 384 fs
LEGEND:
LMEAS
LSIM - Total
LSIM – REF
LSIM – VCO
LSIM - OPSTG
Phase Noise dBc/Hz

## Slide 13: Closed- Loop PLL Transient Noise Simulation
Circuit Inventory
  bsim4v5_0 1133
  bsource_c 277
  bsource_i 481
  capacitor 429
  inductor 196
  mutual inductor 6
  resistor 12
  diode 40
  vsource 78
Accuracy Settings
.option reltol=1e-5 fast=2 $ maxstep=2p delmax=2p
.tran 2p '1024*44*tper'
noisefmax='14e9' noisefmin='300e3’
Simulation Run Time
  11 days on 4 Xeon X5460 @3.16GHz CPUs

## Slide 14: Closed-loop Transient Noise vs. Silicon
Silicon measurements
AFS results

1MHz
Dominated by REFCLK noise

10MHz
Good match

100MHz
Start seeing buffer noise

1GHz
Buffer noise & test equip noise floor




 1M
 10M
 100M
 1G
Driver Noise (not in Simulation) dominates
Noisy REFCLK on eval board
Only real range for comparison
Refclk Noise (not modelled) dominates
Noise Floor of Measurement Equipment

## Slide 15: Conclusion
Lowest jitter PLL with 100 Gbps data transfer rates
Silicon-proven in TSMC’s 28nm process
Performance characterized with AFS Platform enabling
  Rapid and accurate block-level and top-level analysis
  Good simulation-to-silicon correlation
  Leveraging new full-spectrum device-noise analysis technology
  Improved analog SerDes sign-off flow
  Increased design productivity and reduced risk
BDA-TSMC Device Noise Analysis Sub-flow provided good results in reasonable run-times